## Slide 1: Synerduino STM Target Compilation into Hexfile
Synerduino STM Fork of INAV and the Synerduino Target

## Slide 2
Prepare to Build the Hex File
Download the INAV Release 5.1.0
Release 6.0.0
Release 7.0.0
Release 8.0.0
https://github.com/iNavFlight/inav/tree/release_5.1.0
https://github.com/iNavFlight/inav/tree/6.0.0
First you need to download the INAV release version
These are available in the official github page or Synerflight SynerduinoSTM in download tab
https://github.com/iNavFlight/inav/tree/7.0.0

## Slide 3
https://github.com/xpack-dev-tools/arm-none-eabi-gcc-xpack/releases/
INAV–5.1.0 / INAV-6.0.0
Download the Xpack Release 10.2.1-1.1-Win32-x64
https://github.com/xpack-dev-tools/arm-none-eabi-gcc-xpack/releases/download/v9.2.1-1.1/xpack-arm-none-eabi-gcc-9.2.1-1.1-win32-x64.zip
https://github.com/xpack-dev-tools/arm-none-eabi-gcc-xpack/releases/download/v10.2.1-1.1/xpack-arm-none-eabi-gcc-10.2.1-1.1-win32-x64.zip
These are available in the official github page or Synerflight SynerduinoSTM in download tab
https://github.com/xpack-dev-tools/arm-none-eabi-gcc-xpack/releases/download/v10.3.1-2.2/xpack-arm-none-eabi-gcc-10.3.1-2.2-win32-x64.zip
INAV–7.0.0
Download the Xpack Release 10.3.1-2.2-Win32-x64
INAV–8.0.0
Download the Xpack Release 12.2.1-1.1-Win32-x64
https://github.com/xpack-dev-tools/arm-none-eabi-gcc-xpack/releases/download/v13.2.1-1.1/xpack-arm-none-eabi-gcc-13.2.1-1.1-win32-x64.zip

## Slide 4
After installation Go Create a Workspace folder in your local Drive in my case Drive E , and extract and place the following directories INAV-5.1.0 / INAV-6.0.0 / INAV-7.0.0 /INAV8.0.0 Folder , Xpack folder
Note: I place my Workspace Folder on Drive E: as I was using SSD on my Drive C so not to fill it up

## Slide 5
Create new folder inside
INAV 5.1.0
INAV 6.0.0
INAV 7.0.0
INAV 8.0.0
Directory and Name it build

## Slide 6
xpack-arm-none-eabi-gcc-10.2.1-1.1 is extracted to the Xpack folder
INAV 5.1.0 INAV 6.0.0
Inside the Xpack Folder Extract the xpack-arm-none-eabi-gcc -10.2.1-1.1
xpack-arm-none-eabi-gcc-10.3.1-2.2 is extracted to the Xpack folder
INAV 7.0.0
Create an xplack folder in Workspace folder and place it in there
xpack-arm-none-eabi-gcc-13.2.1-1.1 is extracted to the Xpack folder
INAV 8.0.0

## Slide 7
Download the Synerduino Target Folder and Extract to Local drive and place it in the following
(E/Workspace/inav-5.1.0/scr/main/target)
(E/Workspace/inav-6.0.0/scr/main/target)
(E/Workspace/inav-7.0.0/scr/main/target)
(E/Workspace/inav-8.0.0/scr/main/target)
Readme file is also available in the download
System_stm32f4xx.c – is modify to suit the Synerduino STM
INAV 7.0.0 when F411 BP became official)
INAV 8.0.0 F411 discontinued due to size limitation

## Slide 8
Other Download of the Synerduino Target Folder is the sensor driver this is also Extract to Local drive and place it in the following
(E/Workspace/inav-5.1.0/scr/main/drivers/accgyro) ,
(E/Workspace/inav-6.0.0/scr/main/drivers/accgyro) ,
(E/Workspace/inav-7.0.0/scr/main/drivers/accgyro)
(E/Workspace/inav-7.1.0/scr/main/drivers/accgyro)
(E/Workspace/inav-8.0.0/scr/main/drivers/accgyro)
Readme file is also available in the download (accgyro_BMI160) is also modify to use with the SynerduinoSTM shield

## Slide 9
https://www.msys2.org/wiki/MSYS2-installation/
https://xpack.github.io/arm-none-eabi-gcc/
General Info
This is a guide on how to use Windows MSYS2 distribution and building platform to build iNav firmware. This environment is very simple to manage and does not require installing docker for Windows which may get in the way of VMWare or any other virtualization software you already have running for other reasons. Another benefit of this approach is that the compiler runs natively on Windows, so performance is much better than compiling in a virtual environment or a container.
Download Arm Embedded GCC toolkit from The xPack Project
Download MSYS2 for your architecture (most likely 64-bit)
Install and Run msys2-x86

## Slide 10
pacman -S git ruby make cmake gcc mingw-w64-x86_64-libwinpthread-git unzip wget
Copy and paste this script to install Ruby ,Cmake , Make and Gcc

## Slide 11
pacman -S git ruby make cmake gcc mingw-w64-x86_64-libwinpthread-git unzip wget
Y to Proceed installation

## Slide 12
pacman -S git ruby make cmake gcc mingw-w64-x86_64-libwinpthread-git unzip wget
After installation

## Slide 13
cat /e/Workspace/inav-5.1.0/cmake/arm-none-eabi-checks.cmake | grep "set(arm_none_eabi_gcc_version" | cut -d\" -f2
To get the toolkit version you need for your INAV version
# for INAV version 5.0.0, 6.1.0 toolchain version needed is 10.2.1
cd /e/Workspace/xpack
Go to Xpack directory by typing
Source the version number that needs to be downloaded
cat /e/Workspace/inav-6.0.0/cmake/arm-none-eabi-checks.cmake | grep "set(arm_none_eabi_gcc_version" | cut -d\" -f2
# for INAV version 7.0.0 , 7.1.2 toolchain version needed is 10.3.1
cat /e/Workspace/inav-7.0.0/cmake/arm-none-eabi-checks.cmake | grep "set(arm_none_eabi_gcc_version" | cut -d\" -f2
cat /e/Workspace/inav-7.1.0/cmake/arm-none-eabi-checks.cmake | grep "set(arm_none_eabi_gcc_version" | cut -d\" -f2
cat /e/Workspace/inav-7.1.2/cmake/arm-none-eabi-checks.cmake | grep "set(arm_none_eabi_gcc_version" | cut -d\" -f2
cat /e/Workspace/inav-8.0.0/cmake/arm-none-eabi-checks.cmake | grep "set(arm_none_eabi_gcc_version" | cut -d\" -f2
# for INAV version 8.0.0 , 8.1.1 toolchain version needed is 13.2.1

## Slide 14
cd /e/Workspace/xpack
Go to Xpack directory by typing

## Slide 15
Build Folder
E/Workspace/INAV-8.0.0/build
If you have an old CMakeFiles folder of a different versions
Delete it before Exporting a new path

## Slide 16
export PATH=/e/Workspace/xpack/xpack-arm-none-eabi-gcc-10.2.1-1.1/bin:$PATH
Set a Path for the Exported GCC to the Environment Pls make sure the directory is same name as the folder
export PATH=/e/Workspace/xpack/xpack-arm-none-eabi-gcc-10.3.1-2.2/bin:$PATH
INAV 5.1.0 – 6.1.0
INAV 7.0.0 – 7.1.2
export PATH=/e/Workspace/xpack/xpack-arm-none-eabi-gcc-13.2.1-1.1/bin:$PATH
INAV 8.0.0

## Slide 17
Go to the build directory by entering this command
cd /e/Workspace/inav-5.1.0/build
cd /e/Workspace/inav-6.1.0/build
cd /e/Workspace/inav-7.0.0/build
cd /e/Workspace/inav-7.1.0/build
cd /e/Workspace/inav-8.0.0/build
cd /e/Workspace/inav-7.1.1/build
cd /e/Workspace/inav-7.1.2/build
cd /e/Workspace/inav-8.0.0-RC3/build

## Slide 18
Cmake ..
This will extract the Cmake into the build folder creating the Environment
You may need to run rm -rf * in build directory if you had any failed previous runs now run cmake

## Slide 19
make SYNERDUINOSTMSV
This will build the Hexfile Targeted the Synerduino board and its settings to the Build Folder the
Hexfile is use as Firmware when loading the configurator
make SYNERDUINOSTM
make SYNERDUINOSTMSV2
make SYNERDUINOSTM2
make SYNERDUINOSTM_F411
INAV6
INAV7
make SYNERDUINOSTM_F405
make SYNERDUINOSTM_H743
INAV8
make SYNERDUINOSTM_H743A

## Slide 20
Once completed the Hexfile can be found on the Build folder

## Slide 21
And… its here .
cd /e/Workspace/inav-5.1.0/build
cd /e/Workspace/inav-6.0.0/build
INAV_6.0.0_SYNERDUINOSTMSV.hex
Open this file in the Configurator as this is the firmware
Find it in the Build folder of the INAV directory
INAV_5.1.0 SYNERDUINOSTMSV.hex
cd /e/Workspace/inav-7.0.0/build
INAV_6.0.0_SYNERDUINOSTM.hex
INAV_7.0.0_ SYNERDUINOSTM_F411.hex
INAV_5.1.0 SYNERDUINOSTM.hex
cd /e/Workspace/inav-7.1.0/build
INAV_8.0.0_ SYNERDUINOSTM_F405.hex
cd /e/Workspace/inav-7.1.1/build
cd /e/Workspace/inav-8.0.0/build